## Slide 1
Project Nr 4
NEST, a Data-driven Building Model
Team:Robert Hop, Marella Pop, Al Whoop
4

## Slide 2
General Model for SolAce
Heat energy at t+1 is Heat energy at t plus Heat increase minus Heat decrease
Heat increase
Space heating delivered to the unit
Radiation shining through the windows
Heat generated by people present in the room
Heat decrease
Heat transfer through the walls
Space cooling delivered to the unit
4
Vertical Farming

## Slide 3
General Model for SolAce
Dependent variable
Change of Heat energy represented by change of Room temperature (= average of temp_room)
Independent variables
Space heating (= heating_power)
Radiation heat represented by (= rad_room)
People heat represented by Presence (= praes_room)
Heat transfer represented by Temperature difference (= temp_diff)
Space cooling (= cooling_power)
4
Vertical Farming

## Slide 4
General Model for SolAce
Calculated measurement variables
temp_room = average of temp_meeting and temp_office
rad_room = irrad * (blinds_height_F1 + blinds_height_F2 + blinds_height_F3 + blinds_height_F4) during 11am and 5pm and 0 outside of these hours
praes_room = maximum of praes_meeting and praes_office
temp_diff = temp_amb - temp_room
4
Vertical Farming

## Slide 5
General Model for SolAce
Calculated time variables
day_of_week = 0 for Monday to 6 for Sunday
is_weekend = true for Saturday and Sunday
hour = hour of time variable
4
Vertical Farming